## Slide 1: Randoms presentation - Innotech Kft.
Bálint Zsolt
Jenei Dávid
TMSZC Perczel Mór Technikum és Kollégium
IT system and application operator

## Slide 2: Introduction

## Slide 3: Bálint Zsolt’s works and completed tasks
Managing and supervising the entire project
Developing a project plan and timeline
Configuring and installing network devices
Developing security protocols
Documentation
Other protocols
Telnet, SSH
Domain

## Slide 4: Jenei Dávid’s works and completed tasks
Network topology and architecture design
Network infrastructure design (selecting appropriate devices, cabling technology, wireless solutions
Performing cabling or creating a wireless network
Testing
Recording test cases
Error logging

## Slide 5: Network structure
Large-scale network
10 locations
Multiple workflows per location
Transparent, clean structure

## Slide 6: Our fictional company- Innotech Kft.
Our company is a fictional game developer company
Performing multiple work phases per site :
  Engineering
  Game Design
  Sound and VFX
  Marketing
  Media Management

## Slide 7: Central server room
Firewall protection for requests coming from the Internet site
WEB, HTTP, MAIL, DNS server
Central Admin PC
Telnet access to central router
The company's website also runs from here (innotech.hu)

## Slide 8: Site structure
3 VLANs on each site
ACL list between VLANs
Separate DHCP pool for each VLAN (e.g. 10.1.10.0/24)
Wireless network
Admin computer

## Slide 9: NAT

## Slide 10: Access List
An Access list is a collection of rules that, in our case, allows different VLANs to not reach each other
The last two lines in each access-list show that DHCP traffic is allowed

## Slide 11: VPN – GRE Tunnel solution
Secure logical connection between VLAN70 and VLAN80
Use of GRE Tunnel between the two routers
Communication between VLANs over public network
Static routing on the tunnel interface
DHCP-based IP address allocation in both VLANs
The solution is scalable and can be expanded with IPsec encryption later

## Slide 12: Internet simulation (Cloud)
Connection to the US site is handled by an ISP internet simulation.
Frame Relay in the Cloud.

## Slide 13: Dynamic routing(RIP V2)
We use RIP V2 protocol for traffic routing between the company's routers.

## Slide 14: American headquarters location - Porta
In America, there is a port at the headquarters site
IPV6 DHCP address assignment
Not connecting to the network

## Slide 15: American headquarters
Due to the involvement of foreign workers, there are also locations in America, and just like in Hungary, there is a central location here.
DNS, WEB, FTP, MAIL servers
Firewall to control requests to the ISP
Own website (innotech.com)
Admin PC to manage the entire network

## Slide 16: JIRA
Timesheet Tracking extension
Assign tasks

## Slide 17: Github
Project File Storage
Backups
Logs

## Slide 18: Testing
Total 100 tests
Improved testing in case of failed test
Check entire network

## Slide 19: Thank you for your attention!